## Slide 2: Tutorial: Impedance
Sergio Calatroni & Benoît Salvant- CERN

## Slide 3: Tutorial
Goals
  Get acquainted with the main concepts related to beam impedance
  Understand the effect of different materials, and different geometries
Means
  Experimental measurements with Vector Network Analyser (VNA)
  Sincere thanks to Jean-Jacques Gratier from Keysight / Computer Controls for kindly providing a E5080A VNA for free for the school
  Computational exercises with CST Studio Suite and ImpedanceWake2D (IW2D)
  Sincere thanks to Monika Balk from CST / 3DS for providing several free full licenses for Studio Suite for the duration of the school
  Short explanations of theoretical background
The students group will be divided in two for the experimental work
Computer work will be done in teams of 2.

## Slide 4: Plan of the tutorial
Introduction
  Surface impedance (10’ Sergio)
  Recap on beam impedance, introduction to CST studio Suite and IW2D (20’ Benoît)
Work with network analyser 1 (60’ Sergio)
  Measurement of induction of different materials with solenoid
  Identification of materials and coatings
And in parallel: first practice with CST Studio Suite (60’ Benoît)
  Different runs on predefined models: tubes, cavities, bellows…
Guided simulations with IW2D (30’)
  Dependence of impedance on chamber diameter, bunch length, coating, …
Work with network analyser 2 (30’)
  Measurement of resonances (with/without RF fingers)
And in parallel: simulations à la carte (30’)
Ice-cream break

## Slide 5: What is impedance?
A term with many meanings, depending on context
  Impedance in electrical circuits
  Impedance of materials
  Surface impedance
  Beam coupling impedance
There is a common rationale:
  Voltage and current flowing in the circuit, the material, the surface
  The beam current, and the potential it generates on the vacuum pipe

## Slide 6: Square resistance and surface resistance
Consider a square sheet of metal and calculate its resistance to a transverse current flow:
This is the so-called square resistance often indicated as
current
d
a
a

## Slide 7: Square resistance and surface resistance
And now imagine that instead of DC we have RF, and the RF current is confined in a skin depth:
This is a (simplified) definition of surface resistance Rs

current
d
a
a

## Slide 8: Surface impedance
;
S=d2
V~
y
z
x

## Slide 9: Normal metals in the local limit
(in DC)

## Slide 10: Surface impedance practice
For a bulk metal:
Thin film over a substrate (metal)?
  Depends on substrate
  Depends on thickness wrt skin depth
Practice: open two-layers.xlsx
  Thanks to Patrick Krkotić and Uwe Niedermayer for the paper “Iterative Model for Calculating the Surface Impedance of Multilayers”, 2016

## Slide 11: Coil measurement from 100 kHz to 2 MHz

## Slide 12: How the measurement is done
We’ll measure S11
(i.e. S11) power from port 1 going back into port 1
If no power dissipated by the coil:
Output from VNA is always in dB =
What happens when we put a material (with or without coating!) facing the coil?

## Slide 13: Cavity measurement with Keysight VNA up to 1.5 GHz

## Slide 14: How the measurement is done
We’ll measure S21
(i.e. S21) power from port 1 going into port 2
Output from VNA is always in dB =
Compare modules with perfect and damaged fingers
How to identify a resonance?

## Slide 15: Impedance in accelerators

## Slide 16: Impedance: image charges
Image charges flow on the surface of the beampipe
The wakefields potential is proportional to surface impedance of the vacuum chamber surface

## Slide 17: Bunch frequency spectrum: LHC case
Gaussian bunches of 1011 protons, 8 cm long
Beam instantaneous image current
Line spacing: revolution frequency (11 KHz for LHC)
From: E. Métral
Frequency spectrum (Fourier transform)
Real bunches
Power dissipation from wakes is
where is a summation of
over the bunch frequency spectrum
( is the accelerator circumference)
( is the vacuum chamber circumference)

## Slide 18: Transverse impedance
F. Sacherer in: Proceedings of the First Course of the International School of Particle Accelerators, CERN 77-13, p. 198

## Slide 19: From wakefields to impedance
Wakefields have an effect on beam stability, in particular the transverse plane
Risetime of resistive-wall instability depends on the transverse impedance
with at the frequency of the unstable mode

## Slide 20: Betatron motion – simplified model
Unperturbed motion of single particle with and
Adding a perturbation to the beam that changes focussing:
Quadrupoles give the restoring (focussing) force -> harmonic oscillations
Growth rate of instability

## Slide 21: Anomalous skin effect

## Slide 22: Limits for conductivity and skin effect
1. Normal skin effect if:
e.g.: high temperature, low frequency
2. Anomalous skin effect if:
e.g.: low temperature, high frequency
Note: 1 & 2 valid under the implicit assumption
1 & 2 can also be rewritten (in advanced theory) as:
It derives that 1 can be true for and also for

## Slide 23: Mean free path and skin depth
Skin depth
Mean free path

## Slide 24: Anomalous skin effect
Understood by Pippard, Proc. Roy. Soc. A191 (1947) 370
Exact calculations Reuter, Sondheimer, Proc. Roy. Soc. A195 (1948) 336
Normal skin effect
Anomalous skin effect
Asymptotic value

## Slide 25: Two-layers

## Slide 26: Iterative model